## Slide 1: Physiological Noise Correction for fMRI
Lars Kasper
April 30th , 2014
- an Introduction to the PhysIO Toolbox

## Slide 2: The PhysIO Toolbox
    Developed at the Translational Neuromodeling Unit (TNU) since 2008
      Lead programmer: Lars Kasper (TNU)
      Contributors: Jakob Heinzle (TNU), Steffen Bollmann (KiSpi Zurich)
    Part of the TNU «TAPAS» software suite
    Used at the TNU, in Zurich and beyond by ~30 researchers
    Current version:
      http://www.translationalneuromodeling.org/tapas/
    Documentation & Example Data:
      http://www.translationalneuromodeling.org/software/documentation/
      http://www.translationalneuromodeling.org/software/tapas-data/

## Slide 3: fMRI = Acquiring Movies
…of three-dimensional Blood Oxygen-Level Dependent (BOLD) contrast images
Run/Session: Time Series of Images
y
x
z
…
scan 1
time
scan N
Task
Task
No Task
Notes: slice 21…after warping…slice 34 before

## Slide 4: fMRI = Acquiring Movies
Run/Session: Time Series of Images
…
scan 1
time
scan N
The Localized Time-series is the Fundamental Information Unit of fMRI
Signal: Fluctuation through Blood oxygen level dependent (BOLD) contrast
Noise: All other fluctuations
Notes: slice 21…after warping…slice 34 before

## Slide 5: Noise Categories & Reduction
Noise: All other fluctuations
Thermal Noise
  temporally uncorrelated
  reduced SNR  risk of false negatives
  Remedy: Spatial Smoothing
“Structured” Noise
  temporally correlated
  reduced SNR  risk of false negatives
  correlated with task risk of false positives
  Remedy: Noise Modelling (e.g. GLM)
Inference = Signal-To-Noise
Notes: slice 21…after warping…slice 34 before

## Slide 6: The Problem: Physiological Noise
  Cardiac effects
  Respiratory effects

## Slide 7: The Problem: Physiological Noise
  Cardiac effects
    Systole:
      Blood pumped into brain, vessel volume increases: pulsatile vessels
      CSF pushed down: pulsatile CSF
    Diastole:
      Vessel volume decreases
      CSF flows back into “void” brain volume
A Cardiac Cycle in the Brain

## Slide 8: The Problem: Physiological Noise
  Cardiac effects
Vessel Anatomy
Locations
of Fluctuations

## Slide 9: The Problem: Physiological Noise
  Cardiac effects
  Respiratory effects
    Chest (&head) moves with respiratory cycle
    Changes in lung volume change encoding magnetic field for MR
      Geometric distortion/scaling
    Respiratory-sinus arrythmia
      Heart beats faster during inhalation

## Slide 10: Relevance for Neuromodulation
VTA (DA)
Locus coeruleus (NA)
Raphe Nuclei (5-HT)

## Slide 11: Group Level Impact PhysIO
  Andreea Diaconescu (TNU): Social Learning Experiment 2012-2014

## Slide 12: When? – PhysIO experience
  Andreea Diaconescu (TNU): Social Learning
    Higher sensitivity for group effects (N=35)
      Prediction of advice reliability: dmPFC, bilateral FFA
      Prediction error: dmPFC
    Less false/ambiguous positives:
      Brainstem (Substantia Nigra)

## Slide 13: When? – PhysIO experience
  Andreea Diaconescu (TNU): Social Learning
    Higher sensitivity for group effects (N=35)
      Prediction of advice reliability: dmPFC, bilateral FFA
      Prediction error: dmPFC
    Less false/ambiguous positives:
      Brainstem (Substantia Nigra)

## Slide 14: When? – PhysIO experience
  Andreea Diaconescu (TNU): Social Learning
    Higher sensitivity for group effects (N=35)
      Prediction of advice reliability: dmPFC, bilateral FFA
      Prediction error: dmPFC
    Less false/ambiguous positives:
      Brainstem (Substantia Nigra)

## Slide 15: When? – PhysIO experience
  Andreea Diaconescu (TNU): Social Learning
    Higher sensitivity for group effects (N=35)
      Prediction of advice reliability: dmPFC, bilateral FFA
      Prediction error: dmPFC
    Less false/ambiguous positives:
      Brainstem (Substantia Nigra)

## Slide 16: When? – Literature Evidence
  Resting-state:
      Birn, R. M. “The Role of Physiological Noise in Resting-state Functional Connectivity.” NeuroImage 62, 2012
      Birn, R. M., et al. “Separating Respiratory-variation-related Fluctuations from Neuronal-activity-related Fluctuations in fMRI.” NeuroImage 31, 2006
  Task-based:
      Hutton, C., et al. “The Impact of Physiological Noise Correction on fMRI at 7 T.” NeuroImage 57, 2011:

## Slide 17: The Solution: Image-based Physiological Noise Correction
PhysIO Toolbox

## Slide 18: Noise Modelling
Cardiac/respiratory phase
Respiratory Response Function
RETROspective Image CORrection
Cardiac Response Function
Heart Rate
Resp. Volume per Time
convolved with CRF
convolved with RRF
Fourier expansion (cosine/sine)
evaluated at 1 time point (slice) per volume = regressor

## Slide 19: Noise Modelling
Respiratory Response Function
RETROspective Image CORrection
Cardiac Response Function
Cardiac/respiratory phase

## Slide 20: Noise Modelling: Fourier Phase Expansion
cosine and sine to allow for constant phase shifts per voxel
higher model orders to account for under-sampling of physiological frequencies with typical TR in fMRI
cos φ
sin φ
cos 2φ
sin 2φ
cos 3φ
sin 3φ
scans

## Slide 21: Noise Modelling
Respiratory Response Function
RETROspective Image CORrection
Cardiac Response Function
Heart Rate
Heart Rate Variability Response Regressor
convolved with CRF

## Slide 22: Noise Modelling
Respiratory Response Function
RETROspective Image CORrection
Cardiac Response Function
Respiratory Volume per Time
convolved with RRF
Respiratory Volume per Time Regressor

## Slide 23: The Solution: Physiological Noise Correction
1. Physiological Monitoring
2. Preprocessing of Physiological Data
3. Model time series physiological noise
4. Noise Reduction and Assessment
Peripheral Devices
PhysIO Toolbox
SPM
ECG, PPU  Cardiac cycle
Breathing belt  Respiratory cycle
Confound regressors

## Slide 24: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Of peripheral physiological data
Vendor-specific
RETROICOR
Respiratory Volume
Heart Rate
Include confound regressors (GLM)
Filter noisy ECG & detect cardiac pulses
Hand-pick missing pulses
Multiple_regressors file for SPM
Check Influence of Physiological Noise (Correction) on Data
SPM
F-contrast on 1st and second level
Finally:

## Slide 25: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Include confound regressors (GLM)

## Slide 26: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Include confound regressors (GLM)
SCANPHYSLOG.log
One line every 2 ms
…

## Slide 27: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Include confound regressors (GLM)
  Misdetectedheartbeats
  Align scan timing to physiological time series
Notes: TODO: better example w/ actually missed heartbeats

## Slide 28: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Include confound regressors (GLM)
  Cardiac & respiratory phase estimation
  Regressors via Fourier expansion of phases: RETROspective Image CORrection (RETROICOR)

## Slide 29: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Include confound regressors (GLM)

## Slide 30: Model Check: SPM F-contrasts
Check Influence of Physiological Noise (Correction) on Data
SPM
F-contrast on 1st and second level
Finally:
  Cardiac regressors
  Respiratory regressors
  Cardiac x Respiratory
  Movement regressors

## Slide 31: References
        Birn, Rasmus M., Jason B. Diamond, Monica A. Smith, and Peter A. Bandettini. 2006. “Separating Respiratory-variation-related Fluctuations from Neuronal-activity-related Fluctuations in fMRI.” NeuroImage 31 (4) (July 15): 1536–1548. doi:10.1016/j.neuroimage.2006.02.048.
        Glover, G H, T Q Li, and D Ress. 2000. “Image-based Method for Retrospective Correction of Physiological Motion Effects in fMRI: RETROICOR.” Magnetic Resonance in Medicine: Official Journal of the Society of Magnetic Resonance in Medicine / Society of Magnetic Resonance in Medicine 44 (1) (July): 162–7.
        Harvey, Ann K., Kyle T.S. Pattinson, Jonathan C.W. Brooks, Stephen D. Mayhew, Mark Jenkinson, and Richard G. Wise. 2008. “Brainstem Functional Magnetic Resonance Imaging: Disentangling Signal from Physiological Noise.” Journal of Magnetic Resonance Imaging 28 (6): 1337–1344. doi:10.1002/jmri.21623.
        Hutton, C., O. Josephs, J. Stadler, E. Featherstone, A. Reid, O. Speck, J. Bernarding, and N. Weiskopf. 2011. “The Impact of Physiological Noise Correction on fMRI at 7 T.” NeuroImage 57 (1) (July 1): 101–112. doi:10.1016/j.neuroimage.2011.04.018.
        Josephs, O., Howseman, A.M., Friston, K., Turner, R., 1997. “Physiological noise modelling for multi-slice EPI fMRI using SPM.” Proceedings of the 5th Annual Meeting of ISMRM, Vancouver, Canada, p. 1682
        Kasper, Lars, Sarah Marti, S. Johanna Vannesjö, Chloe Hutton, Ray Dolan, Nikolaus Weiskopf, Klaas Enno Stephan, and Klaas Paul Prüssmann. 2009. “Cardiac Artefact Correction for Human Brainstem fMRI at 7 Tesla.” In Proc. Org. Hum. Brain Mapping 15, 395. San Francisco.